By default the inverter sends no CAN messages. You can instruct it to do so via the cantx command

cantx param canid bitstart bits gain
So to send udc on canid 100 (decimal) in bits 0-31 with a gain of 10 (i.e. 100mV resolution):

cantx udc 100 0 32 10

Also this version has CANOpen implemented. You can send so called SDO messages:

Id    Len cmd  index  subindex data
0x601 8   0x40 0x2000 paramidx value

cmd is 1 byte, index is 2 bytes (little endian), subindex 1 byte, data 4 bytes.
The subindex is the parameter index, which is a bit hard to find right now. Basically if you type
"list" you count at which position the parameter shows up. For example boost has subindex 0 because
its the very first.
The value is the desired value*32. So if you want to set boost to 2000 you would send
Id    Len cmd  index     subindex data
0x601 8   0x40 0x00 0x20 0x00     0x00 0xFA 0x00 0x00

2000*32 in hex is 0xFA00

You can also get parameter values:
Id    Len cmd  index  subindex data
0x601 8   0x22 0x2000 paramidx XXX

both read and write messages are acknowledged.